## Slide 1: Fast-Batched Optimal Solution for RTOPF
James, Mert, Vishal

## Slide 2: Introduction

## Slide 3: Introduction
Optimal Power Flow problem (OPF): Deciding the optimal operating conditions (minimizing power generation cost) for a power-plant based on (predicted) demand.
Real-Time OPF (RT-OPF): Solving the problem in real time – matter of minutes/seconds! - Traditional OPF solvers can't handle it
  Renewable energy generators – introduce uncertainty
Two-fold problem:
  Handle uncertainty (run more scenarios!)
  Accelerate solution process
Solution given by the paper:
  A distributed implementation of PDIPM – 3 kernels

## Slide 4: Methods

## Slide 5: Methods
CPU

## Slide 6: Methods
Kernal 1 Setup
  Calculation of partial derivatives of the objective and constraints.
  Lagrangians are computed and the matrix is generated
    Additionally, as our matrices are stored in CSR format, matrix concatenation is a more complicated business
CPU

## Slide 7: Methods
Computation of M and N values for cuSolver input
  Once again using CoDiPack to compute the Derivatives
  Using BLAS to compute the M and N values

## Slide 8: Methods
First Derivative Computation
  Derivatives were computed using CoDiPack's RealForward type

## Slide 9: Methods
2nd Derivative Computation
Derivatives were computed using CoDiPack's evalHessian

## Slide 10: Methods
Kernal 3 Setup
  The solved linear equation is used to compute and evaluate the update steps for the decision variables for the next iteration
CPU

## Slide 11: Methods
Kernal 2 Setup
  This is the most compute intensive set as it involves matrix inversion (solving of a linear system of equations). This is accomplished using CuSolver
    Solves for ΔX and Δλ
GPU

## Slide 12: Methods
cuSparse and cuSolverSp
  cuSparse: Provides primitives for sparse matrix operations (e.g., CSR format) crucial for handling large sparse matrices efficiently.
  cuSolverSp: Specializes in solving sparse linear algebra systems using factorization methods including QR decomposition
QR Decomposition Overview
  QR decomposition is used to factorize matrix A to efficiently solve linear systems Ax=b and least squares problems.
  Our paper utilizes batched QR solutions to handle dynamic adjustments in power systems with high renewable integration.
Matrix Construction:
  From our previous computational process steps, we obtain a large sparse matrix A in column-major format and vector b representing the system states.
Problem Formulation:
  Solve for x in Ax=b, where A is derived from system dynamics and constraints influenced by renewable energy sources
Conversion to CSR Format
  CSR (Compressed Sparse Row) format optimizes non-zero matrix entries storage, reducing memory usage and computation time.
  We convert the A matrix from column-major to CSR format, enabling efficient use of cuSolverSp routines.
cuSolver and cuSparse

## Slide 13: Methods
Set up cuSolver and cuSparse contexts, define matrix descriptions.
Perform structural analysis on A&b using cusolverSpXcsrqrAnalysisBatched.
cuSolver Computational Steps Overview

## Slide 14: Methods
Execute QR decomposition with cusolverSpDcsrqrsvBatched to solve Ax=b.
Fetch the solution vector x from GPU to CPU
cuSolver Computational Steps Overview

## Slide 15: Progress and Current Results

## Slide 16: Results
Solving for Cases 14
Utilized CVXPY, a Python-embedded modeling language for convex optimization problems (CPU)
  Compared performance using SCS and OSQP solvers
Utilized cuSolverSparse, an NVIDIA sparse matrix solver (GPU)
  Factorization
Solver | Solution Time (s) | Speedup (OSQP baseline)
SCS | 0.02 | 1.00
OSQP | 0.0089 | 2.25
cuSolverSparse | 0.05* | 0.4*
Notes: Mention

## Slide 17: Further Research

## Slide 18: Further Research
RealForwardCUDA
  Improve ability to perform parallelized Automatic Differentiation
    Further expand to nested differentiation for nth order derivatives
BLAS package improved utilization
  Improve ability to perform operations
    Matrix Concatenation
    Diagonal/Full Matrix Inversion
Increased Type Safety
  Reduce excessive type shifting
    Current code is very type sensitive, requiring operations to change matrices to pointers, vectors to pointers, pointers to vectors, etc.
cuSolver Batched Mode
  Were unable to use 100% of cuSolver's power to solve many problems at once
    Current implementation performed one 1 type of problem